## Slide 1: Fitting & Matching Region Representation Image Alignment, Optical Flow
Lectures 5 & 6 – Prof. Fergus
Slides from: S. Lazebnik, S. Seitz, M. Pollefeys, A. Effros.

## Slide 2: Panoramas
Facebook 360 photos

## Slide 3: How do we build panorama?
We need to match (align) images

## Slide 4: Matching with Features
Detect feature points in both images

## Slide 5: Matching with Features
Detect feature points in both images
Find corresponding pairs

## Slide 6: Matching with Features
Detect feature points in both images
Find corresponding pairs
Use these pairs to align images

## Slide 7: Matching with Features
Detect feature points in both images
Find corresponding pairs
Use these pairs to align images

## Slide 8: Recall: Edge detection
f
Source: S. Seitz
Edge
Derivative of Gaussian
Edge = maximum of derivative

## Slide 9: Edge detection, Take 2
f
Edge
Second derivative of Gaussian (Laplacian)
Edge = zero crossing of second derivative
Source: S. Seitz

## Slide 10: From edges to blobs
Edge = ripple
Blob = superposition of two ripples
Spatial selection: the magnitude of the Laplacian response will achieve a maximum at the center of the blob, provided the scale of the Laplacian is “matched” to the scale of the blob
maximum

## Slide 11: Scale selection
We want to find the characteristic scale of the blob by convolving it with Laplacians at several scales and looking for the maximum response
However, Laplacian response decays as scale increases:
Why does this happen?
increasing σ
original signal (radius=8)

## Slide 12: Scale normalization
The response of a derivative of Gaussian filter to a perfect step edge decreases as σ increases
Notes: The area under the first derivative of Gaussian from –infinity to 0 is equal to the value of the Gaussian at zero

## Slide 13: Scale normalization
The response of a derivative of Gaussian filter to a perfect step edge decreases as σ increases
To keep response the same (scale-invariant), must multiply Gaussian derivative by σ
Laplacian is the second Gaussian derivative, so it must be multiplied by σ2

## Slide 14: Effect of scale normalization
Scale-normalized Laplacian response
Unnormalized Laplacian response
Original signal
maximum

## Slide 15: Blob detection in 2D
Laplacian of Gaussian: Circularly symmetric operator for blob detection in 2D

## Slide 16: Blob detection in 2D
Laplacian of Gaussian: Circularly symmetric operator for blob detection in 2D
Scale-normalized:

## Slide 17: Scale selection
At what scale does the Laplacian achieve a maximum response to a binary circle of radius r?
r
image
Laplacian

## Slide 18: Scale selection
At what scale does the Laplacian achieve a maximum response to a binary circle of radius r?
To get maximum response, the zeros of the Laplacian have to be aligned with the circle
Zeros of Laplacian is given by (up to scale):
Therefore, the maximum response occurs at
r
image
circle
Laplacian

## Slide 19: Characteristic scale
We define the characteristic scale of a blob as the scale that produces peak of Laplacian response in the blob center
characteristic scale
T. Lindeberg (1998). "Feature detection with automatic scale selection." International Journal of Computer Vision 30 (2): pp 77--116.

## Slide 20: Scale-space blob detector
Convolve image with scale-normalized Laplacian at several scales
Find maxima of squared Laplacian response in scale-space

## Slide 21: Scale-space blob detector: Example

## Slide 22: Scale-space blob detector: Example

## Slide 23: Scale-space blob detector: Example

## Slide 24: Matching with Features
Detect feature points in both images
Find corresponding pairs
Use these pairs to align images

## Slide 25: Scale Invariant Feature Transform
Basic idea:
  Take 16x16 square window around detected feature
  Compute edge orientation (angle of the gradient - 90) for each pixel
  Throw out weak edges (threshold gradient magnitude)
  Create histogram of surviving edge orientations
Adapted from slide by David Lowe
0
2
angle histogram
Former NYU faculty & Prof. Ken Perlin’s advisor
David Lowe IJCV 2004

## Slide 26: Orientation Histogram
4x4 spatial bins (16 bins total)
Gaussian center-weighting
8-bin orientation histogram per bin
8 x 16 = 128 dimensions total
Normalized to unit norm

## Slide 27: Feature stability to affine change
Match features after random change in image scale & orientation, with 2% image noise, and affine distortion
Find nearest neighbor in database of 30,000 features

## Slide 28: Distinctiveness of features
Vary size of database of features, with 30 degree affine change, 2% image noise
Measure % correct for single nearest neighbor match

## Slide 29: SIFT – Scale Invariant Feature Transform1
Empirically found2 to show very good performance, invariant to image rotation, scale, intensity change, and to moderate affine transformations
1 D.Lowe. “Distinctive Image Features from Scale-Invariant Keypoints”. Accepted to IJCV 2004 2 K.Mikolajczyk, C.Schmid. “A Performance Evaluation of Local Descriptors”. CVPR 2003
Scale = 2.5 Rotation = 450

## Slide 30: SIFT invariances
Spatial binning gives tolerance to small shifts in location and scale
Explicit orientation normalization
Photometric normalization by making all vectors unit norm
Orientation histogram gives robustness to small local deformations

## Slide 31: Summary of SIFT
Extraordinarily robust matching technique
  Can handle changes in viewpoint
    Up to about 60 degree out of plane rotation
  Can handle significant changes in illumination
    Sometimes even day vs. night (below)
  Fast and efficient—can run in real time
  Lots of code available
    http://people.csail.mit.edu/albert/ladypack/wiki/index.php/Known_implementations_of_SIFT

## Slide 32: Matching with Features
Detect feature points in both images
Find corresponding pairs
Use these pairs to align images

## Slide 33: Overview
Fitting techniques
  Least Squares
  Total Least Squares
RANSAC
Hough Voting
Alignment as a fitting problem

## Slide 34: Fitting
Source: K. Grauman
Choose a parametric model to represent a set of features
simple model: lines
simple model: circles
complicated model: car

## Slide 35: Fitting: Issues
Noise in the measured feature locations
Extraneous data: clutter (outliers), multiple lines
Missing data: occlusions
Case study: Line detection
Slide: S. Lazebnik

## Slide 36: Fitting: Issues
If we know which points belong to the line, how do we find the “optimal” line parameters?
  Least squares
What if there are outliers?
  Robust fitting, RANSAC
What if there are many lines?
  Voting methods: RANSAC, Hough transform
What if we’re not even sure it’s a line?
  Model selection
Slide: S. Lazebnik

## Slide 37: Overview
Fitting techniques
  Least Squares
  Total Least Squares
RANSAC
Hough Voting
Alignment as a fitting problem

## Slide 38: Least squares line fitting
Data: (x1, y1), …, (xn, yn)
Line equation: yi = m xi + b
Find (m, b) to minimize
(xi, yi)
y=mx+b
Slide: S. Lazebnik

## Slide 39: Least squares line fitting
Data: (x1, y1), …, (xn, yn)
Line equation: yi = m xi + b
Find (m, b) to minimize
Normal equations: least squares solution to XB=Y
(xi, yi)
y=mx+b
Slide: S. Lazebnik

## Slide 40: Matlab Demo
%%%% let's make some points
n = 10;
true_grad = 2;
true_intercept = 3;
noise_level = 0.04;
x = rand(1,n);
y = true_grad*x + true_intercept + randn(1,n)*noise_level;
figure; plot(x,y,'rx');
hold on;
%%% make matrix for linear system
X = [x(:) ones(n,1)];
%%% Solve system of equations
p = inv(X'*X)*X'*y(:); % Pseudo-inverse
p = pinv(X) * y(:); % Pseduo-inverse
p = X \ y(:); % Matlab's \ operator
est_grad = p(1);
est_intercept = p(2);
plot(x,est_grad*x+est_intercept,'b-');
fprintf('True gradient: %f, estimated gradient: %f\n',true_grad,est_grad);
fprintf('True intercept: %f, estimated intercept: %f\n',true_intercept,est_intercept);

## Slide 41: Problem with “vertical” least squares
Not rotation-invariant
Fails completely for vertical lines
Slide: S. Lazebnik

## Slide 42: Overview
Fitting techniques
  Least Squares
  Total Least Squares
RANSAC
Hough Voting
Alignment as a fitting problem

## Slide 43: Total least squares
Distance between point (xi, yi) and line ax+by=d (a2+b2=1): |axi + byi – d|
(xi, yi)
ax+by=d
Unit normal: N=(a, b)
Slide: S. Lazebnik

## Slide 44: Total least squares
Distance between point (xi, yi) and line ax+by=d (a2+b2=1): |axi + byi – d|
Find (a, b, d) to minimize the sum of squared perpendicular distances
(xi, yi)
ax+by=d
Unit normal: N=(a, b)

## Slide 45: Total least squares
Distance between point (xi, yi) and line ax+by=d (a2+b2=1): |axi + byi – d|
Find (a, b, d) to minimize the sum of squared perpendicular distances
(xi, yi)
ax+by=d
Unit normal: N=(a, b)
Solution to (UTU)N = 0, subject to ||N||2 = 1: eigenvector of UTU associated with the smallest eigenvalue (least squares solution to homogeneous linear system UN = 0)
Slide: S. Lazebnik

## Slide 46: Total least squares
second moment matrix
Slide: S. Lazebnik

## Slide 47: Total least squares
N = (a, b)
second moment matrix
Slide: S. Lazebnik

## Slide 48: Least squares: Robustness to noise
Least squares fit to the red points:
Slide: S. Lazebnik

## Slide 49: Least squares: Robustness to noise
Least squares fit with an outlier:
Problem: squared error heavily penalizes outliers
Slide: S. Lazebnik

## Slide 50: Robust estimators
General approach: minimize ri (xi, θ) – residual of ith point w.r.t. model parameters θ ρ – robust function with scale parameter σ
The robust function ρ behaves like squared distance for small values of the residual u but saturates for larger values of u
Slide: S. Lazebnik

## Slide 51: Choosing the scale: Just right
The effect of the outlier is minimized
Slide: S. Lazebnik
Notes: Fit to earlier data with an appropriate choice of s

## Slide 52: Choosing the scale: Too small
The error value is almost the same for every point and the fit is very poor
Slide: S. Lazebnik

## Slide 53: Choosing the scale: Too large
Behaves much the same as least squares

## Slide 54: Overview
Fitting techniques
  Least Squares
  Total Least Squares
RANSAC
Hough Voting
Alignment as a fitting problem

## Slide 55: RANSAC
Robust fitting can deal with a few outliers – what if we have very many?
Random sample consensus (RANSAC): Very general framework for model fitting in the presence of outliers
Outline
  Choose a small subset of points uniformly at random
  Fit a model to that subset
  Find all remaining points that are “close” to the model and reject the rest as outliers
  Do this many times and choose the best model
M. A. Fischler, R. C. Bolles. Random Sample Consensus: A Paradigm for Model Fitting with Applications to Image Analysis and Automated Cartography. Comm. of the ACM, Vol 24, pp 381-395, 1981.
Slide: S. Lazebnik
Notes: This algorithm contains concepts that are hugely useful; in my experience, everyone with some
experience of applied problems who doesn’t yet know RANSAC is almost immediately able to use it to simplify some problem they’ve seen.

## Slide 56: RANSAC for line fitting
Repeat N times:
Draw s points uniformly at random
Fit line to these s points
Find inliers to this line among the remaining points (i.e., points whose distance from the line is less than t)
If there are d or more inliers, accept the line and refit using all inliers
Source: M. Pollefeys

## Slide 57: Choosing the parameters
Initial number of points s
  Typically minimum number needed to fit the model
Distance threshold t
  Choose t so probability for inlier is p (e.g. 0.95)
  Zero-mean Gaussian noise with std. dev. σ: t2=3.84σ2
Number of samples N
  Choose N so that, with probability p, at least one random sample is free from outliers (e.g. p=0.99) (outlier ratio: e)
Source: M. Pollefeys

## Slide 58: Choosing the parameters
Initial number of points s
  Typically minimum number needed to fit the model
Distance threshold t
  Choose t so probability for inlier is p (e.g. 0.95)
  Zero-mean Gaussian noise with std. dev. σ: t2=3.84σ2
Number of samples N
  Choose N so that, with probability p, at least one random sample is free from outliers (e.g. p=0.99) (outlier ratio: e)
 | proportion of outliers e |  |  |  |  |  | 
s | 5% | 10% | 20% | 25% | 30% | 40% | 50%
2 | 2 | 3 | 5 | 6 | 7 | 11 | 17
3 | 3 | 4 | 7 | 9 | 11 | 19 | 35
4 | 3 | 5 | 9 | 13 | 17 | 34 | 72
5 | 4 | 6 | 12 | 17 | 26 | 57 | 146
6 | 4 | 7 | 16 | 24 | 37 | 97 | 293
7 | 4 | 8 | 20 | 33 | 54 | 163 | 588
8 | 5 | 9 | 26 | 44 | 78 | 272 | 1177
Source: M. Pollefeys

## Slide 59: Choosing the parameters
Initial number of points s
  Typically minimum number needed to fit the model
Distance threshold t
  Choose t so probability for inlier is p (e.g. 0.95)
  Zero-mean Gaussian noise with std. dev. σ: t2=3.84σ2
Number of samples N
  Choose N so that, with probability p, at least one random sample is free from outliers (e.g. p=0.99) (outlier ratio: e)
Source: M. Pollefeys

## Slide 60: Choosing the parameters
Initial number of points s
  Typically minimum number needed to fit the model
Distance threshold t
  Choose t so probability for inlier is p (e.g. 0.95)
  Zero-mean Gaussian noise with std. dev. σ: t2=3.84σ2
Number of samples N
  Choose N so that, with probability p, at least one random sample is free from outliers (e.g. p=0.99) (outlier ratio: e)
Consensus set size d
  Should match expected inlier ratio
Source: M. Pollefeys

## Slide 61: Adaptively determining the number of samples
Inlier ratio e is often unknown a priori, so pick worst case, e.g. 50%, and adapt if more inliers are found, e.g. 80% would yield e=0.2
Adaptive procedure:
  N=∞, sample_count =0
  While N >sample_count
    Choose a sample and count the number of inliers
    Set e = 1 – (number of inliers)/(total number of points)
    Recompute N from e:
    Increment the sample_count by 1
Source: M. Pollefeys

## Slide 62: RANSAC pros and cons
Pros
  Simple and general
  Applicable to many different problems
  Often works well in practice
Cons
  Lots of parameters to tune
  Can’t always get a good initialization of the model based on the minimum number of samples
  Sometimes too many iterations are required
  Can fail for extremely low inlier ratios
  We can often do better than brute-force sampling
Source: M. Pollefeys

## Slide 63: Voting schemes
Let each feature vote for all the models that are compatible with it
Hopefully the noise features will not vote consistently for any single model
Missing data doesn’t matter as long as there are enough features remaining to agree on a good model

## Slide 64: Overview
Fitting techniques
  Least Squares
  Total Least Squares
RANSAC
Hough Voting
Alignment as a fitting problem

## Slide 65: Hough transform
An early type of voting scheme
General outline:
  Discretize parameter space into bins
  For each feature point in the image, put a vote in every bin in the parameter space that could have generated this point
  Find bins that have the most votes
P.V.C. Hough, Machine Analysis of Bubble Chamber Pictures, Proc. Int. Conf. High Energy Accelerators and Instrumentation, 1959
Image space
Hough parameter space

## Slide 66: Parameter space representation
A line in the image corresponds to a point in Hough space
Image space
Hough parameter space
Source: S. Seitz

## Slide 67: Parameter space representation
What does a point (x0, y0) in the image space map to in the Hough space?
Image space
Hough parameter space
Source: S. Seitz

## Slide 68: Parameter space representation
What does a point (x0, y0) in the image space map to in the Hough space?
  Answer: the solutions of b = –x0m + y0
  This is a line in Hough space
Image space
Hough parameter space
Source: S. Seitz

## Slide 69: Parameter space representation
Where is the line that contains both (x0, y0) and (x1, y1)?
Image space
Hough parameter space
(x0, y0)
(x1, y1)
b = –x1m + y1
Source: S. Seitz

## Slide 70: Parameter space representation
Where is the line that contains both (x0, y0) and (x1, y1)?
  It is the intersection of the lines b = –x0m + y0 and b = –x1m + y1
Image space
Hough parameter space
(x0, y0)
(x1, y1)
b = –x1m + y1
Source: S. Seitz

## Slide 71: Parameter space representation
Problems with the (m,b) space:
  Unbounded parameter domain
  Vertical lines require infinite m

## Slide 72: Parameter space representation
Problems with the (m,b) space:
  Unbounded parameter domain
  Vertical lines require infinite m
Alternative: polar representation
Each point will add a sinusoid in the (,) parameter space

## Slide 73: Algorithm outline
Initialize accumulator H to all zeros
For each edge point (x,y) in the image For θ = 0 to 180 ρ = x cos θ + y sin θ H(θ, ρ) = H(θ, ρ) + 1 end end
Find the value(s) of (θ, ρ) where H(θ, ρ) is a local maximum
  The detected line in the image is given by ρ = x cos θ + y sin θ
ρ
θ

## Slide 74: Basic illustration
features
votes
Notes: Figure 15.1, top half. Note that most points in the vote array are very dark, because they
get only one vote.

## Slide 75: Other shapes
Square
Circle

## Slide 76: Several lines

## Slide 77: A more complicated image
http://ostatic.com/files/images/ss_hough.jpg

## Slide 78: Effect of noise
features
votes
Notes: This is 15.1 lower half

## Slide 79: Effect of noise
features
votes
Peak gets fuzzy and hard to locate
Notes: This is 15.1 lower half

## Slide 80: Effect of noise
Number of votes for a line of 20 points with increasing noise:
Notes: This is the number of votes that the real line of 20 points gets with increasing noise (figure15.3)

## Slide 81: Random points
Uniform noise can lead to spurious peaks in the array
features
votes
Notes: 15.2; main point is that lots of noise can lead to large peaks in the array

## Slide 82: Random points
As the level of uniform noise increases, the maximum number of votes increases too:
Notes: Figure 15.4; as the noise increases in a picture without a line, the number of points in the max cell goes
up, too

## Slide 83: Dealing with noise
Choose a good grid / discretization
  Too coarse: large votes obtained when too many different lines correspond to a single bucket
  Too fine: miss lines because some points that are not exactly collinear cast votes for different buckets
Increment neighboring bins (smoothing in accumulator array)
Try to get rid of irrelevant features
  Take only edge points with significant gradient magnitude

## Slide 84: Hough transform for circles
How many dimensions will the parameter space have?
Given an oriented edge point, what are all possible bins that it can vote for?

## Slide 85: Hough transform for circles
x
y
(x,y)
x
y
r
image space
Hough parameter space

## Slide 86: Generalized Hough transform
We want to find a shape defined by its boundary points and a reference point
D. Ballard, Generalizing the Hough Transform to Detect Arbitrary Shapes, Pattern Recognition 13(2), 1981, pp. 111-122.
a

## Slide 87: Generalized Hough transform
p
We want to find a shape defined by its boundary points and a reference point
For every boundary point p, we can compute the displacement vector r = a – p as a function of gradient orientation θ
D. Ballard, Generalizing the Hough Transform to Detect Arbitrary Shapes, Pattern Recognition 13(2), 1981, pp. 111-122.
a
θ
r(θ)

## Slide 88: Generalized Hough transform
For model shape: construct a table indexed by θ storing displacement vectors r as function of gradient direction
Detection: For each edge point p with gradient orientation θ:
  Retrieve all r indexed with θ
  For each r(θ), put a vote in the Hough space at p + r(θ)
Peak in this Hough space is reference point with most supporting edges
Assumption: translation is the only transformation here, i.e., orientation and scale are fixed
Source: K. Grauman

## Slide 89: Overview
Fitting techniques
  Least Squares
  Total Least Squares
RANSAC
Hough Voting
Alignment as a fitting problem

## Slide 90: Image alignment
Two broad approaches:
  Direct (pixel-based) alignment
    Search for alignment where most pixels agree
  Feature-based alignment
    Search for alignment where extracted features agree
    Can be verified using pixel-based alignment
Source: S. Lazebnik

## Slide 91: Alignment as fitting
Previously: fitting a model to features in one image
Find model M that minimizes
M
xi
Source: S. Lazebnik

## Slide 92: Alignment as fitting
Previously: fitting a model to features in one image
Alignment: fitting a model to a transformation between pairs of features (matches) in two images
Find model M that minimizes
Find transformation T that minimizes
M
xi
T
xi
xi
'
Source: S. Lazebnik

## Slide 93: 2D transformation models
Similarity (translation, scale, rotation)
Affine
Projective (homography)
Source: S. Lazebnik

## Slide 94: Let’s start with affine transformations
Simple fitting procedure (linear least squares)
Approximates viewpoint changes for roughly planar objects and roughly orthographic cameras
Can be used to initialize fitting for more complex models
Source: S. Lazebnik

## Slide 95: Fitting an affine transformation
Assume we know the correspondences, how do we get the transformation?
Source: S. Lazebnik

## Slide 96: Fitting an affine transformation
Linear system with six unknowns
Each match gives us two linearly independent equations: need at least three to solve for the transformation parameters
Source: S. Lazebnik

## Slide 97: Feature-based alignment outline

## Slide 98: Feature-based alignment outline
Extract features

## Slide 99: Feature-based alignment outline
Extract features
Compute putative matches

## Slide 100: Feature-based alignment outline
Extract features
Compute putative matches
Loop:
  Hypothesize transformation T

## Slide 101: Feature-based alignment outline
Extract features
Compute putative matches
Loop:
  Hypothesize transformation T
  Verify transformation (search for other matches consistent with T)

## Slide 102: Feature-based alignment outline
Extract features
Compute putative matches
Loop:
  Hypothesize transformation T
  Verify transformation (search for other matches consistent with T)

## Slide 103: Dealing with outliers
The set of putative matches contains a very high percentage of outliers
Geometric fitting strategies:
  RANSAC
  Hough transform

## Slide 104: RANSAC
RANSAC loop:
Randomly select a seed group of matches
Compute transformation from seed group
Find inliers to this transformation
If the number of inliers is sufficiently large, re-compute least-squares estimate of transformation on all of the inliers
Keep the transformation with the largest number of inliers

## Slide 105: RANSAC example: Translation
Putative matches
Source: A. Efros

## Slide 106: RANSAC example: Translation
Select one match, count inliers
Source: A. Efros

## Slide 107: RANSAC example: Translation
Select one match, count inliers
Source: A. Efros

## Slide 108: RANSAC example: Translation
Select translation with the most inliers
Source: A. Efros

## Slide 109: Motion estimation techniques
Feature-based methods
  Extract visual features (corners, textured areas) and track them over multiple frames
  Sparse motion fields, but more robust tracking
  Suitable when image motion is large (10s of pixels)
Direct methods
  Directly recover image motion at each pixel from spatio-temporal image brightness variations
  Dense motion fields, but sensitive to appearance variations
  Suitable for video and when image motion is small

## Slide 110: Optical flow
Combination of slides from Rick Szeliski, Steve Seitz, Alyosha Efros and Bill Freeman and Fredo Durand

## Slide 111: Motion estimation: Optical flow
Will start by estimating motion of each pixel separately
Then will consider motion of entire image

## Slide 112: Why estimate motion?
Lots of uses
  Track object behavior
  Correct for camera jitter (stabilization)
  Align images (mosaics)
  3D shape reconstruction
  Special effects

## Slide 113: Problem definition: optical flow
How to estimate pixel motion from image H to image I?
  Solve pixel correspondence problem
    given a pixel in H, look for nearby pixels of the same color in I
Key assumptions
  color constancy: a point in H looks the same in I
    For grayscale images, this is brightness constancy
  small motion: points do not move very far
This is called the optical flow problem

## Slide 114: Optical flow constraints (grayscale images)
Let’s look at these constraints more closely
  brightness constancy: Q: what’s the equation?
  small motion: (u and v are less than 1 pixel)
    suppose we take the Taylor series expansion of I:
H(x,y)=I(x+u, y+v)
Notes: A: H(x,y) = I(x+u, y+v)

## Slide 115: Optical flow equation
Combining these two equations
In the limit as u and v go to zero, this becomes exact

## Slide 116: Optical flow equation
Q: how many unknowns and equations per pixel?
Intuitively, what does this constraint mean?
  The component of the flow in the gradient direction is determined
  The component of the flow parallel to an edge is unknown
This explains the Barber Pole illusion
  http://www.sandlotscience.com/Ambiguous/Barberpole_Illusion.htm
  http://www.liv.ac.uk/~marcob/Trieste/barberpole.html
2 unknowns, one equation
http://en.wikipedia.org/wiki/Barber's_pole
Notes: A: u and v are unknown, 1 equation

## Slide 117: Aperture problem

## Slide 118: Aperture problem

## Slide 119: Solving the aperture problem
How to get more equations for a pixel?
  Basic idea: impose additional constraints
    most common is to assume that the flow field is smooth locally
    one method: pretend the pixel’s neighbors have the same (u,v)
      If we use a 5x5 window, that gives us 25 equations per pixel!

## Slide 120: RGB version
How to get more equations for a pixel?
  Basic idea: impose additional constraints
    most common is to assume that the flow field is smooth locally
    one method: pretend the pixel’s neighbors have the same (u,v)
      If we use a 5x5 window, that gives us 25*3 equations per pixel!
Note that RGB is not enough to disambiguate because R, G & B are correlated Just provides better gradient

## Slide 121: Lukas-Kanade flow
Prob: we have more equations than unknowns
  The summations are over all pixels in the K x K window
  This technique was first proposed by Lukas & Kanade (1981)
Solution: solve least squares problem
  minimum least squares solution given by solution (in d) of:

## Slide 122: Aperture Problem and Normal Flow
The gradient constraint:
Defines a line in the (u,v) space
u
v
Normal Flow:

## Slide 123: Combining Local Constraints
u
v
etc.

## Slide 124: Conditions for solvability
  Optimal (u, v) satisfies Lucas-Kanade equation
When is This Solvable?
  ATA should be invertible
  ATA should not be too small due to noise
    eigenvalues l1 and l2 of ATA should not be too small
  ATA should be well-conditioned
    l1/ l2 should not be too large (l1 = larger eigenvalue)
ATA is solvable when there is no aperture problem

## Slide 125: Eigenvectors of ATA
Recall the Harris corner detector: M = ATA is the second moment matrix
The eigenvectors and eigenvalues of M relate to edge direction and magnitude
  The eigenvector associated with the larger eigenvalue points in the direction of fastest intensity change
  The other eigenvector is orthogonal to it
Notes: Suppose M = vv^T . What are the eigenvectors and eigenvalues? Start by considering Mv

## Slide 126: Interpreting the eigenvalues
1
2
“Corner” 1 and 2 are large, 1 ~ 2
1 and 2 are small
“Edge” 1 >> 2
“Edge” 2 >> 1
“Flat” region
Classification of image points using eigenvalues of the second moment matrix:

## Slide 127: Local Patch Analysis

## Slide 128: Edge
large gradients, all the same
large l1, small l2

## Slide 129: Low texture region
gradients have small magnitude
small l1, small l2

## Slide 130: High textured region
gradients are different, large magnitudes
large l1, large l2

## Slide 131: Observation
This is a two image problem BUT
  Can measure sensitivity by just looking at one of the images!
  This tells us which pixels are easy to track, which are hard
    very useful later on when we do feature tracking...

## Slide 132: Motion models
Translation
2 unknowns
Affine
6 unknowns
Perspective
8 unknowns
3D rotation
3 unknowns

## Slide 133: Affine motion
Substituting into the brightness constancy equation:

## Slide 134: Affine motion
Substituting into the brightness constancy equation:
Each pixel provides 1 linear constraint in 6 unknowns
Least squares minimization:

## Slide 135: Errors in Lukas-Kanade
What are the potential causes of errors in this procedure?
  Suppose ATA is easily invertible
  Suppose there is not much noise in the image
When our assumptions are violated
  Brightness constancy is not satisfied
  The motion is not small
  A point does not move like its neighbors
    window size is too large
    what is the ideal window size?

## Slide 136: Iterative Refinement
Iterative Lukas-Kanade Algorithm
  Estimate velocity at each pixel by solving Lucas-Kanade equations
  Warp H towards I using the estimated flow field
    - use image warping techniques
  Repeat until convergence

## Slide 137: Optical Flow: Iterative Estimation
x
x0
Initial guess:
Estimate:
estimate update
(using d for displacement here instead of u)

## Slide 138: Optical Flow: Iterative Estimation
x
x0
estimate update
Initial guess:
Estimate:

## Slide 139: Optical Flow: Iterative Estimation
x
x0
Initial guess:
Estimate:
Initial guess:
Estimate:
estimate update

## Slide 140: Optical Flow: Iterative Estimation
x
x0

## Slide 141: Optical Flow: Iterative Estimation
Some Implementation Issues:
  Warping is not easy (ensure that errors in warping are smaller than the estimate refinement)
  Warp one image, take derivatives of the other so you don’t need to re-compute the gradient after each iteration.
  Often useful to low-pass filter the images before motion estimation (for better derivative estimation, and linear approximations to image intensity)

## Slide 142: Revisiting the small motion assumption
Is this motion small enough?
  Probably not—it’s much larger than one pixel (2nd order terms dominate)
  How might we solve this problem?

## Slide 143: Optical Flow: Aliasing
Temporal aliasing causes ambiguities in optical flow because images can have many pixels with the same intensity.
I.e., how do we know which ‘correspondence’ is correct?
nearest match is correct (no aliasing)
nearest match is incorrect (aliasing)
To overcome aliasing: coarse-to-fine estimation.
actual shift
estimated shift

## Slide 144: Reduce the resolution!

## Slide 145: Coarse-to-fine optical flow estimation
image I
image H
Gaussian pyramid of image H
Gaussian pyramid of image I
image I
image H
u=10 pixels
u=5 pixels
u=2.5 pixels
u=1.25 pixels

## Slide 146: Coarse-to-fine optical flow estimation
image I
image J
Gaussian pyramid of image H
Gaussian pyramid of image I
image I
image H
run iterative L-K
run iterative L-K
warp & upsample
.
.
.

## Slide 147: Recap: Classes of Techniques
Feature-based methods (e.g. SIFT+Ransac+regression)
  Extract visual features (corners, textured areas) and track them over multiple frames
  Sparse motion fields, but possibly robust tracking
  Suitable especially when image motion is large (10-s of pixels)
Direct-methods (e.g. optical flow)
  Directly recover image motion from spatio-temporal image brightness variations
  Global motion parameters directly recovered without an intermediate feature motion calculation
  Dense motion fields, but more sensitive to appearance variations
  Suitable for video and when image motion is small (< 10 pixels)