Agenda for Computational Thought 07OCT2009:

Discussion of Adder

Flip-flop

Puzzle

Class began with a review on the previous discussion of the adder, which is diagrammed below:

Carry in i Carry Out i+1

Input A

Input B Position i bit

Combinations that return 1:

| Carry | In A | In B |
| --- | --- | --- |
| 1 | 0 | 0 |
| 0 | 1 | 0 |
| 0 | 0 | 1 |
| 1 | 1 | 1 |

The carry out for the adder will be 1 only if there are 2 or 3 ones in any of the 3 inputs, which can be represented by this circuit:

Several adders linked in a ripple setup:

This creates a long clock, which in turn affects computer speed and efficiency.

An analogy to this is like trying to pass a message across a room and you have to tell the person next to you to pass the message to the person next to them until it reaches the end of the chain, which can take a very long time depending on the length of the chain. The same is true for the ripple adder.

A solution to this is to create two local adders that do the calculations for both cases whether the carry is 1 or 0

The side that doesn’t have the right carry in will be zero so the result is dependant on the opposite.

Gate = 1 so the second and gate will return 0 and x will return through the first and gate as well as through the or gate.

This approach trades more circuits for a shorter path and so this will ultimately result in a faster time to process this command.

This is useful in computing for speeding up the process of various operations in computing by pre-computing all possible operations for specific numbers so that when an operation is given the result will only have to be processed by a few logic gates.

With the ripple adders it gets very long:

In carry look-ahead adders all of the circuits send data to another circuit, which will determine the result.

In order for adders to help us however we need a way to hold information with circuits this is where flip-flops come into play.

Computers today utilize Clocked Digital Binary Circuits

A clock at 2 GHz will produce a signal 2 billion times per second.

Data is stored in a register at every clock cycle.

Registers ( 2 billion times per second

Cache ( .5-1 billion times per second

RAM ( 5 million times per second

Disk ( 1 thousand times per second

Register:

Feedback is created by the and gate that will loop a data bit when the clock is down and once the clock is up a new data bit is inserted into the loop

Assignment for Monday is the Burton Smith Chapter in Out of their Minds and the Lego tower problem in the puzzle book.

# Text boxes

xor

result

B

xor

Carry in

A

or

or

and

and

and

Carry out

Carry

B

B

A

A

Carry

This ripple adder can carry all the way to an indefinite number of adders

Position 1 out

0

A1

B1

The carry has the longest path and it has to go through at least 3 logic gates

This may not seem like much but it can add up over several adders

Ex.

63 x 3 +2=191 logic gates

Position 2 out

A2

B2

or

Carry in

and

Carry in

not

and

Local adder/1

Local adder/0

and

X: if gate =1

Y: if gate = 0

or

and

y

Gate

x

Not Gate

5v

1 clock cycle

0v

more

faster

Register

Cache

RAM

Disk

clock

not

Data bit

clock

and

or

and